Piper Cherokee Warrior II (PA 28-161).

Technical Specifications.

# Lycoming Engine : 160 Hp

Four cylinder, direct-drive, horizontally opposed, air cooled engine

Fixed-pitch propeller

Fuel Capacity : 50 US Gallons

Oil Capacity : 8 US Quarts

Maximum Takeoff and Landing Weight : 2 325 lb

Wing Loading : 13.7 lbs / square foot

Maximum Baggage : 200 lbs

Never Exceed Speed (Vne) : 160 mph

Maximum Cruising Speed (Vno) : 126 mph

Maximum Flaps Extended Speed (Vfe) : 103 mph

Instrument Markings :

Tachometer : 500 – 2 700 rpm

Oil Temperature : 75 – 245 deg, F

Oil Pressure : 60 – 90 PSI (Normal)

Best Rate Of Climb : 80 mph

Best Angle Of Climb : 63 mph

Maximum Flap Speed : 103 mph

Stall warning sounds at 5 – 10 kts above stall speed

Pitot-static System :

Supplies both pitot and static pressure for the :

- Airspeed Indicator

- Altimeter

- Vertical Speed Indicator